## Slide 1: Introduction to Verilog HDL

## Slide 2
HDL?
HDL stands for "Hardware Description Language." It is a specialized computer language used to describe the structure and behavior of digital electronic circuits, such as microprocessors, ASICs (Application-Specific Integrated Circuits), and FPGAs (Field-Programmable Gate Arrays).
The primary purpose of HDLs is to enable designers and engineers to model and simulate complex hardware systems before they are physically implemented in silicon or other hardware technologies. HDLs are essential tools in digital hardware design and are used throughout the entire design flow, from concept and simulation to synthesis and verification.
Popular HDLs are Verilog HDL & VHDL (for any complexity).

## Slide 3: Features of HDLs
Easy development, verification and debugging through HDLs.
HDL descriptions are easily portable, and is also compatible to all design tools.
HDLs can describe the digital systems at various abstraction levels & also supports hierarchical modeling.
HDL descriptions can be functionally simulated with Logic Simulators .
Notes: There are several levels of system description, from Silicon to complex system description and these levels can be analyzed both in terms of their structure and behavior. The several levels of system description are: 1.system 2.chip 3. Register 4.gate 5.circuit and 6.silicon.
Schematics come under structural representation and the range of system descriptions can be from circuit level to system level description.
Boolean equations come under behavioral representation and only the gate level system description is possible.
HDL descriptions come under behavioral representation and, both the register level and gate level system descriptions are possible.

## Slide 4: Features of HDLs
Easy development, verification and debugging through HDLs.
HDL descriptions are easily portable, and is also compatible to all design tools.
HDLs can describe the digital systems at various abstraction levels & also supports hierarchical modeling.
HDL descriptions can be functionally simulated with Logic Simulators .
Notes: Logic synthesis tools convert the RTL description to a gate-level netlist. A gate-level netlist is a description of the circuit in terms of gates and connections between them.
With the advent of logic synthesis the digital circuits could be described at an abstract level in terms of functionality and data flow by use of an HDL, and the details of the gates and their interconnections to implement the circuit were automatically extracted by logic synthesis tools from the design description.
The gate-level netlist is input to an automatic place and route tool, which creates a layout. The layout is verified and then fabricated on the chip.

## Slide 5
History of Verilog
Developed by Philip Moorby in 1984-1985.
Gateway Design Automation introduced Verilog in 1984 as their proprietary HDL.
Cadence took over in 1989.
Cadence made Verilog HDL public in 1990.
Verilog HDL becomes IEEE 1364-1995.

## Slide 6: Popularity of Verilog HDL
Verilog HDL is modeled after ‘C’ language.
Allows different levels of abstraction to be mixed in the same model.
Easy to learn and easy to use.
Almost all logic simulation & synthesis tools support Verilog.
Verilog HDL is an IEEE 1364 standard.

## Slide 7: Verilog basics
Verilog HDL is case-sensitive.
All the keywords in Verilog must be in lower case.
Verilog constructs may be written across multiple lines, or on one line.
Notes: All the keywords in verilog should be written in lower-case only.
Any keyword which is not in lower-case is treated as an identifier.
Two identifiers which differ in the case of evan a single character is treated to be another identifier.
Verilog constructs can be written by allowing the white spaces within, and even they can be written across multiple lines by suitably splitting the construct.

## Slide 8: Identifiers and key words
Identifiers and keywords are used to define language constructs.
Identifiers refer objects to be referenced in the design.
Identifiers are made of alphabets (both cases), numbers, the underscore ‘_’ and the dollar sign ‘$’.
They start with an alphabetic character or underscore.

## Slide 9: cont’d..
They cannot start with a number or with ‘$’ which is reserved for system tasks.
Identifiers are case sensitive i.e., identifiers differing in their case are distinct.
An identifier say count is different from COUNT, count and cOuNT.

## Slide 10: Examples of Identifiers
Count
COUNT
_R2_D2
R56_68
FIVE$
$count Illegal
12six_b Illegal
Example:
reg sum;
input data;

## Slide 11: Number specification
Sized numbers.
      <size> ’<base format> <number>
Unsized numbers.
      ’<base format> <number>
<size> in decimal
<base format> can be b or B, d or D, o or O and h or H.
Numbers without <base format> are decimal by default.
Notes: Integer constants i.e. integer numbers specified implicitly are decimal by default. The number can be preceded by a (-)sign if it is a negative value.
Whenever a number is supposed to be written in a non-decimal format, it has to be preceded by a (’) and a letter denoting the base of the number either (h or H), (b or B), or (o or O) and any value specified this way is treated as an unsigned number. These numbers have their size as machine(compiler) specific, but should be at least 32 bits.
But the 32 bit representation of each number takes a lot of memory. Verilog allows the use of sized numbers whereby the user can allocate the required number of bits for the number he is describing.

## Slide 12: cont’d..
Examples:
Sized numbers :
4'b1111 // This is a 4-bit binary number
12'habc // This is a 12-bit hexadecimal number
16'd255 // This is a 16-bit decimal number.
Unsized numbers :
23456 // This is a 32-bit decimal number by default
'hc3 // This is a 32-bit hexadecimal number
'o21 // This is a 32-bit octal number

## Slide 13: Unknown & high impedance values
X or x for unknown values.
Z or z for high impedance values.
X or Z at the MSB has the self padding property.
Examples:
32 ’B z // this is a 32-bit high impedance number
6 ’h X // this is a 6-bit hex number
12 ’H 13x // this is a 12-bit hex number
Notes: A register by default takes the x or X(unknown value) and a wire by default takes the z or Z(high impedance value).
If the number specified is smaller than the size allocated for it, then depending upon the MSB, whether it is a 0 or X or Z, the corresponding leftover higher order bits are automatically padded with 0's, X's and Z's respectively. This rule is not valid for a 1(that is if the MSB is a 1 then no padding with 1's is done for the leftover higher order bits).