## Slide 1: Operators

## Slide 2: Operator types
The operators can be :
  arithmetic
  logical
  relational
  equality
  bit wise
  reduction
  shift
  concatenation
  replication
  conditional

## Slide 3: Arithmetic operators
Expressions constitute operators and operands.
operation | symbol | operand
Multiply | * | binary
Divide | / | binary
Add | + | binary
Subtract | - | binary
Modulus | % | binary

## Slide 4: Arithmetic operator examples
Eg: a * b // multiply a and b
a / b // divide a by b
a+b // add a and b
a - b // subtract b from a
a%b // modulus of a by b
a=3’b011 b=3’b010 d=4 e=3
c=a * b // c= 3’b110
c= a / b // c= 1
c= a+b // c= 3’b101
c= a-b // c=3’b001
c=d/e // c=1

## Slide 5: Cont’d..
13 % 4 // evaluates to 1.
-9 % 2 // evaluates to -1, takes sign of the first //operand
In arithmetic operations, if any operand bit has a
value x, then the result of the entire expression is x.
The size of the result is determined by the size of
the largest operand.

## Slide 6: Logical operators
Logical operator evaluates always to a one bit value either
true(1) or false (0) or x (unambiguous) . If any operand bit
is either x or z it is equivalent to x
operation | symbol | operand
logical and | && | binary
logical or | ¦¦ | binary
logical not | ! | binary

## Slide 7: Logical operator examples
a1 = 1’b0; // 0 is false;
a2 = 1’b1; // 1 is true
a1 && a2 is 0 (false)
a1 || a2 is 1 (true)
!a2 is 0 (false)
For vector operands, a non-zero vector is treated as logical 1.

## Slide 8: Cont’d..
Example:
a=10 b=00
a && b // evaluates to 0 ( 1 && 0)
a=2’b1x b=2’b11
a || b // is unknown, evaluates to x.

## Slide 9: Relational operators
Relational operations return logical 0 or 1. If there is any x or z bit in operand then it will return x.
Operation | Symbol | Operand
greater | > | Binary
less than | < | Binary
Greater than or equal to | >= | Binary
Less than or equal to | <= | Binary

## Slide 10: Relational operator examples
a = 5 b = 6 c = 2’1x
a >b // evaluates to 0
a <= b // evaluates to 1
b >= c // evaluates to x

## Slide 11: Equality operators
Equality operators are the following
Operation | Symbol | Operand
logical equality | == | binary
logical inequality | != | binary
case equality | === | binary
case inequality | !== | binary

## Slide 12: Equality operators
Equality operator can return 1 or 0.
Logical equality operator (== !=) will return x if any of the operand bit has x.
Case equality operator compares both operand bit by bit including x and z bit. If it matches then returns 1 or else it returns 0. It doesn’t return x.

## Slide 13: Cont’d..
a=3; b=5; c=3’b100; d=3’b101; e=4’b1xxx; f=4’b1xxx;
g=3’b1xxz
a !=b // evaluates to 1.
e===f // evaluates to 1.
f===g // evaluates to 0. d == e // evaluates to x

## Slide 14: Bitwise operators
Bitwise operations are performed on each bit of the operand
Operation | Symbol | Operand
Bitwise and | & | Binary
Bitwise or | ¦ | Binary
Bitwise negation | ~ | Unary
Bitwise xor | ^ | Binary
Bitwise xnor | ~^ or ^~ | Binary

## Slide 15: Bitwise operators Example
module fulladd_1(sum,carry,a,b,c);
input a,b,c;
output sum,carry;
wire sum,carry;
assign sum = (a^b )^ c;
assign carry = (a&b) | (b&c) | (c&a);
endmodule

## Slide 16: Bitwise operator examples
a = 3’b111; b = 3’b101; d = 3’b1x1;
c = ~a; // c = 3’b000
c = a & b; // c = 3’b101
c = a | b; // c = 3’b111
c = a ^ b; // c = 3’b010
c = a | d; // c = 3’b1x1

## Slide 17: Reduction operators
Reduction operators are unary operators
Operation | Symbol | Operand
reduction and | & | unary
reduction nand | ~& | unary
reduction or | ¦ | unary
reduction nor | ~¦ | unary
reduction xor | ^ | unary
reduction xnor | ~^ or ~^ | unary

## Slide 18: Reduction operator examples
x = 4’b01100
c = &x // c= 0 & 1&1&0&0 c=0
c = |x // c= 0|1|1|0|0 c=1
c = ^x // c=0^1^1^0^0 c=0

## Slide 19: Shift operators
Shift operator can be shift left or shift right
Example:
a = 4’b1011;
y = a >> 2; // y =4’b0010, 0’s filled in MSB
y = a << 2; // y = 4’b1100, 0’s filled in LSB
Operation | Symbol | Operand
shift right | >> | unary
shift left | << | unary

## Slide 20: Concatenation operators
Concatenation operator is used to append multiple operands.
The operand must be sized.
a=3’b101; b=3’b111;
y = {a,b}; // y = 6’b101111
y = {a,b,3’b010}; // y =101111010

## Slide 21: Replication operators
Replication operator is used to concatenate same
number.
a=3’b101 b =2’b10
y = {2{a}}; // result of y is 6’b101101
y = {2{a},2{b} }; // result of y is 10’b1011011010
y = { 2{a},2’b10}; // result of y is 6’b10110110

## Slide 22: Conditional operators
Conditional operator ? :
format:
conditional_expr ? true expr : false expr;
eg:
assign out = control ? I1 : l2;
control out
1 I1
0 I2

## Slide 23: Conditional Operator examples
module mux_con(out,s0,s1,i);
input s0,s1;
input [3:0]i;
output out;
wire out;
assign out = s1 ? ( s0 ? i[3]:i[2]) : (s0 ? i[1]:i[0]) ;
endmodule

## Slide 24: Operator precedence
+ - ~ !
* / %
+ -
<< >>
< <= > >=
& ~&
^ ~^
| ~|
&&
||
? :
unary
arithmetic
binary
shift
relational
reduction and , nand
reduction exor, exnor
reduction or , nor
logical and
logical or
conditional