## Slide 1
Boolean Algebra and Logic Gate

## Slide 2: George Boole
Father of Boolean algebra
He came up with a type of linguistic algebra, the three most basic operations of which were (and still are) AND, OR and NOT. It was these three functions that formed the basis of his premise, and were the only operations necessary to perform comparisons or basic mathematical functions.
Boole’s system was based on a binary approach, processing only two objects - the yes-no, true-false, on-off, zero-one approach.
Surprisingly, given his standing in the academic community, Boole's idea was either criticized or completely ignored by the majority of his peers.
Eventually, one bright student, claude shunnon(1916-2001), picked up the idea and ran with it
George Boole (1815 - 1864)

## Slide 3: Axiomatic Definition of Boolean Algebra
We need to define algebra for binary values
  Developed by George Boole in 1854
Huntington postulates (1904) for Boolean algebra :
B = {0, 1} and two binary operations, (+) and (.)
  Closure with respect to operator (+) and operator (.)
  Identity element 0 for operator (+) and 1 for operator (.)
  Commutativity with respect to (+) and (.)
    x+y = y+x, x·y = y·x
  Distributivity of (.) over (+), and (+) over (.)
  x·(y+z) = (x·y)+(x·z) and x+(y·z) = (x+y)·(x+z)
        Complement for every element x is x’ with x+x’=1, x·x’=0
  There are at least two elements x,yB such that xy

## Slide 4: Boolean Algebra
Terminology:
  Literal: A variable or its complement
  Product term: literals connected by (·)
  Sum term: literals connected by (+)

## Slide 5: Postulates of Boolean Algebra
B = {0, 1} and two binary operations, (+) and (.)
The rules of operations: AND, OR and NOT.
Closure (+ and‧)
The identity elements
  (1) + = 0
  (2) · = 1
x | y | X.y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
AND
x | y | x+y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
OR
x | X’
0 | 1
1 | 0
NOT

## Slide 6: Postulates of Boolean Algebra
    The commutative laws x+y = y+x, x.y = y.x
    The distributive laws
x | y | z | y+z | x．(y+z) | x．y | x．z | (x．y)+(x．z)
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 7: Postulates of Two-Valued Boolean Algebra
Complement
  x+x'=1 → 0+0'=0+1=1; 1+1'=1+0=1
  x．x'=0 → 0．0'=0．1=0; 1．1'=1．0=0
Has two distinct elements 1 and 0, with 0 ≠ 1
Note
  A set of two elements
  (+) : OR operation; (·) : AND operation
  A complement operator: NOT operation
  Binary logic is a two-valued Boolean algebra

## Slide 8: Duality
The principle of duality is an important concept. This says that if an expression is valid in Boolean algebra, the dual of that expression is also valid.
To form the dual of an expression, replace all (+) operators with (·) operators, all (·) operators with (+) operators, all ones with zeros, and all zeros with ones.
Following the replacement rules…
  a(b + c) = ab + ac
Form the dual of the expression
  a + (bc) = (a + b)(a + c)
Take care not to alter the location of the parentheses if they are present.

## Slide 9: Basic Theorems

## Slide 10: Proof of x+x=x
We can only use Huntington postulates:
Show that x+x=x.
  x+x = (x+x)·1 by 2(b)
  = (x+x)(x+x’) by 5(a)
  = x+xx’ by 4(b)
  = x+0 by 5(b)
  = x by 2(a)
  Q.E.D.
We can now use Theorem 1(a) in future proofs
Huntington postulates:
Post. 2: (a) x+0=x, (b) x·1=x
Post. 3: (a) x+y=y+x, (b) x·y=y·x
Post. 4: (a) x(y+z) = xy+xz, (b) x+yz = (x+y)(x+z)
Post. 5: (a) x+x’=1, (b) x·x’=0

## Slide 11: Absorption Property
Theorem 6(a): x + xy = x
  x + xy = x．1 + xy by 2(b)
  = x (1 + y) 4(a)
  = x (y + 1) 3(a)
  = x．1 Th 2(a)
  = x 2(b)
Theorem 6(b): x (x + y) = x by duality
By means of truth table (another way to proof )
x | y | xy | x+xy
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 1
1 | 1 | 1 | 1
Huntington postulates:
Post. 2: (a) x+0=x, (b) x·1=x
Post. 3: (a) x+y=y+x, (b) x·y=y·x
Post. 4: (a) x(y+z) = xy+xz, (b) x+yz = (x+y)(x+z)
Post. 5: (a) x+x’=1, (b) x·x’=0
Th. 2: (a) x+1=1

## Slide 12: DeMorgan’s Theorem
Theorem 5(a): (x + y)’ = x’y’
Theorem 5(b): (xy)’ = x’ + y’
By means of truth table
x | y | x’ | y’ | x+y | (x+y)’ | x’y’ | xy | x’+y' | (xy)’
0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0

## Slide 13: Consensus Theorem
xy + x’z + yz = xy + x’z
(x+y)•(x’+z)•(y+z) = (x+y)•(x’+z) -- (dual)
Proof:
  xy + x’z + yz
    = xy + x’z + 1.yz 2(a)
    = xy + x’z + (x+x’)yz 5(a)
    = xy + x’z + xyz + x’yz 3(b) &4(a)
    = (xy + xyz) + (x’z + x’zy) Th4(a)
    = x(y + yz) + x’ (z + zy) 4(a)
    = xy + x’z Th6(a)
    QED (2 true by duality).

## Slide 14: Operator Precedence
The operator precedence for evaluating Boolean Expression is
  Parentheses
  NOT
  AND
  OR
Examples
  x y' + z
  (x y + z)'

## Slide 15: 2.5 Boolean Functions
A Boolean function
  Binary variables
  Binary operators OR and AND
  Unary operator NOT
  Parentheses
Examples
  F1= x y z'
  F2 = x + y'z
  F3 = x' y' z + x' y z + x y'
  F4 = x y' + x' z

## Slide 16: Boolean Functions
  The truth table of 2n entries (n=number of variables)
Two Boolean expressions may specify the same function
  F3 = F4
x | y | z | F1 | F2 | F3 | F4
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 1 | 0 | 0

## Slide 17: Boolean Functions
Implementation with logic gates
  F4 is more economical
  F4 = x y' + x' z
  F3 = x' y' z + x' y z + x y'
  F2 = x + y'z

## Slide 18: Algebraic Manipulation
When a Boolean expression is implemented with logic gates, each term requires a gate and each variable (Literal) within the term designates an input to the gate. (F3 has 3 terms and 8 literal)
To minimize Boolean expressions, minimize the number of literals and the number of terms → a circuit with less equipment
  It is a hard problem (no specific rules to follow)
Example 2.1
  x(x'+y) = xx' + xy = 0+xy = xy
  x+x'y = (x+x')(x+y) = 1 (x+y) = x+y
  (x+y)(x+y') = x+xy+xy'+yy' = x(1+y+y') = x
  xy + x'z + yz = xy + x'z + yz(x+x') = xy + x'z + yzx + yzx' = xy(1+z) + x'z(1+y) = xy +x'z
  (x+y)(x'+z)(y+z) = (x+y)(x'+z), by duality from function 4. (consensus theorem with duality)

## Slide 19: Complement of a Function
An interchange of 0's for 1's and 1's for 0's in the value of F
  By DeMorgan's theorem
  (A+B+C)' = (A+X)' let B+C = X
  = A'X' by theorem 5(a) (DeMorgan's)
  = A'(B+C)' substitute B+C = X
  = A'(B'C') by theorem 5(a) (DeMorgan's)
  = A'B'C' by theorem 4(b) (associative)
Generalization: a function is obtained by interchanging AND and OR operators and complementing each literal.
  (A+B+C+D+ ... +F)' = A'B'C'D'... F'
  (ABCD ... F)' = A'+ B'+C'+D' ... +F'

## Slide 20: Examples
Example 2.2
  F1' = (x'yz' + x'y'z)' = (x'yz')' (x'y'z)' = (x+y'+z) (x+y+z')
  F2' = [x(y'z'+yz)]' = x' + (y'z'+yz)' = x' + (y'z')' (yz)‘
  = x' + (y+z) (y'+z')
  = x' + yz‘+y'z
Example 2.3: a simpler procedure
  Take the dual of the function and complement each literal
  F1 = x'yz' + x'y'z.
  The dual of F1 is (x'+y+z') (x'+y'+z).
  Complement each literal: (x+y'+z)(x+y+z') = F1'
  F2 = x(y' z' + yz).
  The dual of F2 is x+(y'+z') (y+z).
  Complement each literal: x'+(y+z)(y' +z') = F2'

## Slide 21: Canonical and Standard Forms
Minterms and Maxterms
A minterm (standard product): an AND term consists of all literals in their normal form or in their complement form.
  For example, two binary variables x and y,
    xy, xy', x'y, x'y'
  It is also called a standard product.
  n variables can be combined to form 2n minterms.
A maxterm (standard sums): an OR term
  It is also call a standard sum.
  2n maxterms.

## Slide 22: Minterms and Maxterms
  Each maxterm is the complement of its corresponding minterm, and vice versa.

## Slide 23
A Boolean function can be expressed algebraically from a given truth table by forming a minterm for each combination of the variables that produces a 1 in the function and then taking the OR of all those terms.
Minterms and Maxterms

## Slide 24: Minterms and Maxterms
An Boolean function can be expressed by
  A truth table
  Sum of minterms for each combination of variables that produces a (1) in the function.
  f1 = x'y'z + xy'z' + xyz = m1 + m4 +m7 (Minterms)
  f2 = x'yz+ xy'z + xyz'+xyz = m3 + m5 +m6 + m7 (Minterms)

## Slide 25: Minterms and Maxterms
The complement of a Boolean function
  The minterms that produce a 0
  f1' = m0 + m2 +m3 + m5 + m6 = x'y'z'+x'yz'+x'yz+xy'z+xyz'
  f1 = (f1')'
  = (x+y+z)(x+y'+z) (x+y'+z') (x'+y+z')(x'+y'+z) = M0 M2 M3 M5 M6
  f2 = (x+y+z)(x+y+z')(x+y'+z)(x'+y+z)=M0M1M2M4
  Any Boolean function can be expressed as terms).
  A product of maxterms (“product” meaning the ANDing of terms).
  A sum of minterms (“sum” meaning the ORing of Both boolean functions are said to be in Canonical form.

## Slide 26: Sum of Minterms
Sum of minterms: there are 2n minterms and 22n combinations of functions with n Boolean variables.
Example 2.4: express F = A+B’C as a sum of minterms.
  F = A+B'C = A (B+B') + B'C = AB +AB' + B'C = AB(C+C') + AB'(C+C') + (A+A')B'C = ABC+ABC'+AB'C+AB'C'+A'B'C
  F = A'B'C +AB'C' +AB'C+ABC'+ ABC = m1 + m4 +m5 + m6 + m7
  F(A, B, C) = S(1, 4, 5, 6, 7)
  or, built the truth table first

## Slide 27: Product of Maxterms
Product of maxterms: using distributive law to expand.
  x + yz = (x + y)(x + z) = (x+y+zz')(x+z+yy') = (x+y+z)(x+y+z')(x+y'+z)
Example 2.5: express F = xy + x'z as a product of maxterms.
  F = xy + x'z = (xy + x')(xy +z) = (x+x')(y+x')(x+z)(y+z) = (x'+y)(x+z)(y+z)
  x'+y = x' + y + zz' = (x'+y+z)(x'+y+z')
  F = (x+y+z)(x+y'+z)(x'+y+z)(x'+y+z') = M0M2M4M5
  F(x, y, z) = P(0, 2, 4, 5)

## Slide 28: Conversion between Canonical Forms
The complement of a function expressed as the sum of minterms equals the sum of minterms missing from the original function.
  F(A, B, C) = S(1, 4, 5, 6, 7)
  Thus, F‘ (A, B, C) = S(0, 2, 3)
  By DeMorgan's theorem
  F(A, B, C) = P(0, 2, 3)
  F'(A, B, C) =P (1, 4, 5, 6, 7)
  mj' = Mj
To convert from one canonical form to another: interchange the symbols S and P and list those numbers missing from the original form
    S of 1's
    P of 0's

## Slide 29
Example
  F = xy + xz
  F(x, y, z) = S(1, 3, 6, 7)
  F(x, y, z) = P (0, 2, 4, 6)

## Slide 30: Standard Forms
In canonical forms each minterm or maxterm must contain all the variables either complemented or uncomplemented, thus these forms are very seldom the ones with the least number of literals.
Standard forms: the terms that form the function may obtain one, two, or any number of literals, .There are two types of standard forms:
  Sum of products: F1 = y' + xy+ x'yz'
  Product of sums: F2 = x(y'+z)(x'+y+z')
A Boolean function may be expressed in a nonstandard form
  F3 = AB + C(D + E)
But it can be changed to a standard form by. using. The distributive law
  F3 = AB + C(D + E) = AB + CD + CE

## Slide 31: Implementation
Two-level implementation
Multi-level implementation
F1 = y' + xy+ x'yz'
F2 = x(y'+z)(x'+y+z')

## Slide 32: 2.8 Digital Logic Gates
Boolean expression: AND, OR and NOT operations
Constructing gates of other logic operations
  The feasibility and economy;
  The possibility of extending gate's inputs;
  The basic properties of the binary operations (commutative and associative);
  The ability of the gate to implement Boolean functions.

## Slide 33: Summary of Logic Gates
Digital logic gates

## Slide 34
Digital logic gates
Summary of Logic Gates

## Slide 35: Multiple Inputs
Extension to multiple inputs
  A gate can be extended to multiple inputs.
    If its binary operation is commutative and associative.
  AND and OR are commutative and associative.
    OR
      x+y = y+x
      (x+y)+z = x+(y+z) = x+y+z
    AND
      xy = yx
      (x y)z = x(y z) = x y z

## Slide 36: Multiple Inputs
Multiple NOR = a complement of OR gate, Multiple NAND = a complement of AND.
The cascaded NAND operations = sum of products.
The cascaded NOR operations = product of sums.
Multiple-input and cascaded NOR and NAND gates

## Slide 37: Multiple Inputs
The XOR and XNOR gates are commutative and associative.
Multiple-input XOR gates are uncommon?
XOR is an odd function: it is equal to 1 if the inputs variables have an odd number of 1's.
3-input XOR gate

## Slide 38: Positive and Negative Logic
Positive and Negative Logic
  Two signal values <=> two logic values
  Positive logic: H=1; L=0
  Negative logic: H=0; L=1
Consider a TTL gates
  A positive logic AND gate
  A negative logic OR gate
Signal assignment and logic polarity

## Slide 39: Positive and Negative Logic

## Slide 40
Functions that have unspecified outputs for some input combinations are called incompletely specified functions.
In most applications, we simply don’t care what value is assumed by the function for the unspecified minterms thus the unspecified minterms of a function are called don’t-care conditions.
These don’t-care conditions can be used on a map to provide further simplification of the Boolean expression.
Donot care terms

## Slide 41
A don’t-care minterm is a combination of variables whose logical value is not specified.
Such a minterm cannot be marked with a 1 in the map, because it would require that the function always be a 1 for such a combination.
Likewise, putting a 0 on the square requires the function to be 0.
To distinguish the don’t-care condition from 1’s and 0’s, an X is used.
In choosing adjacent squares to simplify the function in a map, the don’t-care minterms may be assumed to be either 0 or 1.
Donot care terms