## Slide 1: Combinational Circuits
Mr. Bikash Kumar Behera

## Slide 2: Combinational Logic
Logic circuits for digital systems may be combinational or sequential.
A combinational circuit consists of input variables, logic gates, and output variables.
The outputs are functions of inputs.

## Slide 3: Design Procedure
From the pspecifications of the circuit determine the required number of inputs and outputs and assign a symbol to each.
Derive the truth table that defines the required relationship between inputs and outputs.
Obtain the simplified Boolean functions for each output as a function of the input variables using K-Map.
Draw the logic diagram.

## Slide 4: Half Adder
A combinational circuit that performs the addition of two bits is called a half adder.
The truth table for the half adder is listed below:
A B C S

## Slide 5: Half Adder
A
B

## Slide 6: Full-Adder
One that performs the addition of three bits(two significant bits and a previous carry) is a full adder.
A B Cin Cout S

## Slide 7: Full Adder
BCin
A
BCin
A
Cout

## Slide 8: Full Adder
A
B
Cin
Sum
Cout

## Slide 9: Half Subtractor
Half Subtractor is a combinational logic circuit.
It is used for the purpose of subtracting two single bit numbers.
It contains 2 inputs and 2 outputs (difference and borrow).
X | Y | Difference(D) | Borrow(B)
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0

## Slide 10: Half Subtractor

## Slide 11: Full Subtractor
Full Subtractor is a combinational logic circuit.
Thus, full subtractor has the ability to perform the subtraction of three bits.
Full subtractor contains 3 inputs and 2 outputs (Difference and Borrow)

## Slide 12: Full Subtractor
X | Y | Z | Difference(D) | Borrow(B)
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1

## Slide 13: Full Subtractor

## Slide 14: Full Subtractor
Difference = Z ⊕(X ⊕Y)
Borrow = X'Y + (X ⊕Y)' Z

## Slide 15: Binary adder
This is also called Ripple Carry Adder ,because of the construction with full adders are connected in cascade.

## Slide 16: Carry Propagation
The signal from Ci to the output carry Ci+1, propagates through an AND and OR gates, so, for an n-bit RCA, there are 2n gate levels for the carry to propagate from input to output.
Because the propagation delay will affect the output signals on different time, so the signals are given enough time to get the precise and stable outputs.

## Slide 17: Carry look-ahead Adder

## Slide 18: Carry look-ahead Adder
Pi = Ai ⊕ Bi Carry Propagating term
Gi = AiBi Carry Generating term
Output sum and carry
Si = Pi ⊕ Ci
Ci+1 = Gi + PiCi
Gi : carry generate Pi : carry propagate
C0 = input carry
C1 = G0 + P0C0
C2 = G1 + P1C1 = G1 + P1G0 + P1P0C0
C3 = G2 + P2C2 = G2 + P2G1 + P2P1G0 + P2P1P0C0
C3 does not have to wait for C2 and C1 to propagate.

## Slide 19: 4-bit adder with carry lookahead

## Slide 20: Binary Subtractor

## Slide 21: Binary Adder/Subtractor
M = 1subtractor and M = 0adder

## Slide 22: Decoder
Decoder is a combinational circuit that has ‘N’ input lines and maximum of (2)N unique output lines.
The name “Decoder” means to translate or decode coded information from one format into another, so a digital decoder transforms a set of digital input signals into an equivalent decimal code at its output.

## Slide 23: Decoder
Active High Decoder - The output line that is active will be High(1) and rest all the outputs will be low(0).
Active Low Decoder - The output line that is active will be Low(0) and rest all the outputs will be High(1).

## Slide 24: 2:4 active high Decoder Decoder Basics and 2 to 4 Decodee
I1 | I0 | D0 | D1 | D2 | D3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1

## Slide 25: 2:4 active high Decoder

## Slide 26: 2:4 active low Decoder
I1 | I0 | D0 | D1 | D2 | D3
0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0

## Slide 27: 2:4 active low Decoder
D3
D2
D1
D0
I0
I1

## Slide 28: 3:8 line Decoder 3 to 8 Decoder workinge
I2 | I1 | I0 | D0 | D1 | D2 | D3 | D4 | D5 | D6 | D7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 |  | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 29: 3:8 line Decoder
I0
I1
I2

## Slide 30: Block diagram of 3:8 active high decoder
I1
I0
I2
D0
D1
D2
D3
D4
D5
D6
D7

## Slide 31: 2:4 Active High Decoder with Enable High
E | I1 | I0 | D0 | D1 | D2 | D3
0 | X | X | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 1 | 0
I0
I1
D0
D1
D2
D3
E

## Slide 32: 2:4 Active High Decoder with Enable Low
E | I1 | I0 | D0 | D1 | D2 | D3
0 | 0 | 0 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1 | 0
1 | X | X | 0 | 0 | 0 | 0
I1
I0
D0
D1
D2
D3

## Slide 33: Encoder Encoder in Digital Electronicse
An encoder is the inverse operation of a decoder.
It Converts Decimal to Binary.
At any instant of time only input line should be active.

## Slide 34: 4:2 Encoder

## Slide 35: 4:2 Encoder
D3
D2
D1
B1
B0

## Slide 36: Multiplexer/ Data Selector Multiplexer 2*1, 4:2
Multiplexer is a combinational circuit that has maximum of (2)ndata inputs, ‘n’ selection lines and single output line.
One of these data inputs will be connected to the output based on the values of selection lines.
Since there are ‘n’ selection lines, there will be (2)n possible combinations of zeros and ones.
So, each combination will select only one data input.

## Slide 37: 2X1 Multiplexer
Function Table | 
S | F
0 | I0
1 | I1
Truth Table |  |  | 
S | I1 | I0 | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 38: 4X1 Multiplexer
Function Table |  | 
S1 | S0 | F
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3
F

## Slide 39: Boolean Function Implementation
The inividual minterms can be selected by the data inputs thereby providing a method of implementing a Boolean function of n variables with a multiplexer that has “n” selection inputs and “2n” data inputs one for each minterm .
The minterm of a function are generated in a multiplexer by the circuit associated with the selection inputs.
For implementing any Boolean function of “n” variables with a multiplexer with “(n-1)” selection inputs and “2(n-1)” data inputs follows from the previous example . To begin with, Boolean function is listed in a truth table. Then first “(n-1)” variables in the table are applied to the selection inputs of the multiplexer
Implementation of Boolean Function in Multiplexer | Solved problem – YouTube
Demultiplexer (DEMUX) Digital Decoder | 1 to 4 Demultiplexer | Full Adder using Demux - YouTube