## Slide 2: Rectifier
Rectifier is an electronic device which is used for converting an alternating quantity (Voltage or current) into unidirectional i.e. DC quantity (Voltage or current).
The input to a rectifier is AC, whereas its output is unidirectional or DC.
Every electronic circuit such as amplifiers, needs a DC power source for its operation.
This DC voltage has to be obtained from AC supply.
For this the AC supply has to be reduced,Stepped down first using a Step down transformer and then converted to dc by using rectifier.

## Slide 4: Halfwave Rectifier
  A half wave rectifier is a type of rectifier which allows only half cycle (either positive half cycle or negative half cycle) of the input AC signal while the another half cycle is blocked.
  If the positive half cycle is allowed then the negative half cycle is blocked.
  If the negative half cycle is allowed then the positive half cycle is blocked.
  A half wave rectifier will not allow both positive and negative half cycles at the same time.

## Slide 5: Halfwave Rectifier
    Half-wave rectifier utilizes only alternate half-cycles of the input sinusoid.
    For positive half cycle of input signal, Diode is forward biased & Vo = Vi .
    For negaive half cycle of input signal, Diode is reverse biased & Vo = 0 .

## Slide 6: Halfwave Rectifier

## Slide 9: Average and RMS value

## Slide 10: Efficiency
So efficiency of the half wave rectifier with ideal diode (rf=0) is only 40.4%

## Slide 11: Ripple factor
It speaks about the quality of the dc output of a rectifier.
The ripple factor of a rectifier is defined as the ratio of rms value of ac component in the output to the dc component present in the output.
ripple factor clearly indicates that the output of a half-wave rectifier is of poor quality since it contains more ac components than the required dc components.
or

## Slide 12: Peak Inverse voltage
It is defined as the maximum reverse voltage that a diode can withstand without destroying the junction. The peak inverse voltage across a diode is the peak of the negative half cycle. For half-wave rectifier, PIV is Vm.

## Slide 13: Fullwave Centertap Rectifier

## Slide 14: Center-tapped Transformer Full-wave Rectifier:

## Slide 15: Fullwave Centertap Rectifier
During the positive half-cycle, the upper diode is forward-biased and the lower diode is reverse-biased.

## Slide 16: Fullwave Centertap Rectifier
During the negative half-cycle, the lower diode is forward-biased and the upper diode is reverse-biased.

## Slide 17: Network conditions for the positive and negative region of vi.

## Slide 18: Fullwave Centertap Rectifier

## Slide 20
Peak Inverse
Voltage For each rectifier circuit
there is a maximum voltage to which the diode can be subjected. This potential is called the peak inverse voltage because it occurs during that part of the cycle when the diode is nonconducting.
For the half-wave rectifier, the peak inverse voltage is Vm. For a full-wave circuit, twice this value is obtained.

## Slide 21: PIV of Rectifier
PIV is the maximum reverse voltage that can be applied to
the diode which will not damage the diode.
PIV rating of diode is very much important to design the circuit.
PIV of rectifier can be forund as below.

## Slide 22: Contd...
Particulars | W.H.R | C.T.F.W.R
No. of Diode | 1 | 2
Transformer Requirement | No | Yes
Max. Efficiency | 40.6% | 81.2%
R.F | 1.21 | 0.48
Output frequency | fin | 2fin
PIV | Vm | 2Vm
Comparison of Rectifiers

## Slide 23: Rectifier parameters
  Average Value
  RMS Value
  Efficiency
  Peak inverse voltage
  Ripple factor

## Slide 24: Rectifier parameters
  Efficiency:
  Rectifier efficiency indicates how efficiently the rectifier converts AC into DC.
  A high percentage of rectifier efficiency indicates a good rectifier while a low percentage of rectifier efficiency indicates an inefficient rectifier.
  Rectifier efficiency is defined as the ratio of DC output power to the AC input power(rms).
  HWR FWR

## Slide 25: Rectifier parameters
  Peak inverse voltage(PIV):
  Peak inverse voltage or peak reverse voltage is the maximum voltage a diode can withstand in the reverse bias condition.
  If the applied voltage is greater than the peak inverse voltage, the diode will be permanently destroyed.
  PIV of HWR = Vm
  PIV of FWR = 2Vm (Centertapped transformer FWR)
  = Vm (Bridgetype FWR)

## Slide 26: Rectifier parameters
  Ripple factor:
  The ripple factor is used to measure the amount of ripples present in the output DC signal.
  A high ripple factor indicates a high pulsating DC signal while a low ripple factor indicates a low pulsating DC signal.
  Ripple factor is defined as the ratio of ripple voltage to the pure DC voltage.
  Ripple factor of HWR is 1.21 & FWR is 0.48.