## Slide 2: DC Load line
At cutoff region Ic=0
At saturation region VCE=0
The dc load line is a graph that allows us to determine all possible combinations of IC and VCE for a given amplifier.
The endpoints of the dc load line are labeled IC(sat) and VCE(off) . The collector current and the output voltage can not exceeds this limit

## Slide 3: Operating point or Quiescent(Q)-point
It is the intersection point between the load line and output characteristic curve under a specific value of base current.
The operating point is also called DC point. The Quiescent point meaning it is not having any AC signal only DC biasing signal is there.
It is possible to operate the amplifier at any point along the load line. The best operating point is usually in the center of the load line.

## Slide 4: Biasing
To operate the transistor, it should be operated at a particular operating point. The process of selecting the operating point is called biasing
It is achieved by suitably selecting the DC sources and the resistors to operate the transistor in active region.
To operate the transistor properly as an amplifier, the two pn junctions must be correctly biased with external dc voltages.
In general the DC signal is used for biasing and the input AC signal is to be amplified

## Slide 5
Bias circuits set the dc level at a point that allows the ac signal to vary in both the positive and negative directions without driving the transistor into saturation or cutoff.

## Slide 6
If the level of IB is changed by varying the value of RB the Q-point moves up or down

## Slide 7
Q-point is shifted toward cutoff region:

## Slide 8
If VCC is held fixed and RC changed, the load line will shift as below
If RC is fixed and VCC varied, the load line shifts as below

## Slide 9
The transistor must be biased properly to get undistorted amplified version of input signal
Setting an operating point(Q-point) is the basic criteria of a transistor based amplifier
The Q point is selected in such a way that maximum undistorted signal can be obtained at the output side
Once the Q-point is selected it should not shift the position by changing of IC.
The IC may be changed due to
  Variation of β
  Temperature variation

## Slide 10: Fixed Bias
A simplest way to bias a transistor is called as fixed bias.
It consists of one source and two external resistors
The dc equivalent circuit can be written by replacing the
capacitors with open circuits

## Slide 11
Base-Emitter loop

## Slide 12: Collector-Emitter loop

## Slide 13: Q1. The operating point for a fixed bias circuit is given by VCE = 7 V and IC = 7 mA. In order to achieve this operating point, determine the value of resistors RB and RC. The transistor has VBE = 0.65 V and β = 120.

## Slide 14
Q2. (a) What is Vce when Vin=0V
(b) What is the minimum value of Ib required to saturate the transistor if beta=200
(c) Calculate the maximum value of Rb when Vin=5V

## Slide 15
Q3. Determine the following for the fixed-bias configuration of below circuit. Verify the operation region of transistor
(a) IBQ and ICQ.
(b) VCEQ.
(c) VB and VC.
(d) VBC.

## Slide 16: Q4. In the below circuit find IC, VCC, Beta, and RB
IB = 20 microA ; IE = 4 mA ; VCE = 7.2V ; VBE = 0.7V; RC = 2.2 kohm
(a) IC + IB = IE
IC = IE – IB = 4 mA – 0.02 mA = 3.98 mA
(b) VCC = IC RC + VCE
= (3.98 mA × 2.2kohm) + 7.2 V
= 15.956 V
= 16 V
(c)
(d)

## Slide 17: Q5. Determine the Q-point for the below circuit and draw the dc load line. Find the Find the maximum peak value of base current for linear operation. Assume Beta(dc)=200
The Q-point is at 6.93V and 39.6mA
IC can increase an amount ideally equal to
60.6-39.6=21mA
The maximum peak variation of the base current as

## Slide 18: Q6. Determine whether or not the transistor of below figure, is in saturation. Assume VCE(sat) = 0.2 V.