## Slide 1: Remote Procedure Call - Performance
Lecture-12

## Slide 2: UNIT-2: Communications in Distributed Systems
Basics of Communication Networks
Layered Protocols
ATM Models
Client-Server Models
Blocking and Non-Blocking Primitives
Buffered and Un-Buffered Primitives
Reliable and Unreliable Primitives
Messagepassing
Remote Procedure Calls

## Slide 3: #9: Remote Procedure Call - Performance
Success or failure of a Distributed System depends on its Performance.
  Performance is critically dependent on the “Speed of the Communication*”.
    *: Stands (50+)% & Falls (50- )% with its implementations rather than with its abstract principles.
    One should analyze where the time is spent?
Implementation of Distributed System
  Protocol Selection
  Acknowledgement
  Critical Path
  Copying
  Timer Management

## Slide 4: #9.1:RPC Protocol Selection
Criteria of Selection: It should gets the bits from the client’s kernel to the server’s kernel
Connection-oriented protocol vs Connectionless protocol
Standard general-purpose protocol vs Specifically designed for RPC
Length of Packet and Message

## Slide 5: #9.1.1:Connection-oriented Vs Connectionless Protocol
Connection-Oriented Protocol | Connectionless Protocol
After connection establishment, the client is bound to the server | No principle of connection establishment for long period. However session-wise pairing between two neighboring entities is required.
Same connection is used by all the traffic, in both directions. | The path used by all the traffic might be different
Communication is easier | Communication is easier is LAN, where most of the connections are of one hop length
When a kernel sends a message, the possibility of lost of the message and receiving of its ACK is not worrisome for it. | Loss of message, loss of ACK need extra work
This approach is very strong in WAN | Reliable in LAN
This is not suitable in LAN ( The extra s/w are forming hindrance in the LAN ) | Suitable in small building LAN
Conclusion: Connection-oriented in WAN | Conclusion: Connectionless in LAN
Connection-Oriented Protocol | Connectionless Protocol
After connection establishment, the client is bound to the server | No principle of connection establishment for long period. However session-wise pairing between two neighboring entities is required.
Same connection is used by all the traffic, in both directions. | The path used by all the traffic might be different
Communication is easier | Communication is easier is LAN, where most of the connections are of one hop length
When a kernel sends a message, the possibility of lost of the message and receiving of its ACK is not worrisome for it. | Loss of message, loss of ACK need extra work
This approach is very strong in WAN | Reliable in LAN
 | Suitable in small building LAN
Conclusion: Connection-oriented in WAN | Conclusion: Connectionless in LAN

## Slide 6: #9.1.2:Standard Protocol Vs Specialized RPC
Standard Protocol (IP or UDP) | Specialized RPC
The protocol is already designed. Saves substantial work. | It is need to be invented, implemented, tested and embedded in existing systems. Considerably more work.
Many implementations are available. Saves work and time. | More work and time
Communication is easier | Communication need to be tested in the networks.
Most of the UNIX systems accept the packets of these protocol for communication purpose | Needs integration into existing UNIX systems
Existing networks also support IP and UDP packets | Need to be tested across all types of networks
Writing, executing and testing code using these protocols are straightforward. | Several phases of software testing is required.
IP is not an end-to-end protocol. It is executed on top of reliable TCP. So, it bounce back several times in the network. | Specialized RPC would avoid bouncing back of the packets.
IP has 13 header fields. 3 are essential (Src_Addr, Dstn_addr, Pkt_len). Header checksum is time consuming | Number of header fields may differ, according to the requirement of the problem.

## Slide 7: #9.1.3:Packet and Message Length
Doing an RPC has a large, fixed overhead, independent of the amount of the data sent.
Thus, reading a 64K file in a single 64K RPC is more efficient than reading it in 64 1K RPCs.
It is therefore important that the protocol and network allow large transmissions.
Large size file with Maxflow should be supported by both protocol and network
  Sun Microsystem’s limit is 8K (System level constraints)
  Ethernet’s limit is 1536 bytes (Network level constraints)

## Slide 8: #9.2:Acknowledgements
When large RPCs have to be broken up into many small packets, then what should be the acknowledgement process?
  Should individual packets be acknowledged? (stop-and-wait- protocol)
  Acknowledge after receiving all the packets (Blast Protocol)
*******
*******

## Slide 9: Cont..

## Slide 10: Cont..
Suppose a client want to write a 4K block of data to a file server, but the system cannot handle packets larger than 1K.
The message will be divided int 4 1K size of packets (P0-P3).
In the Stop-and-wait protocol, the client will send P0, then waits for an acknowledgement from the server.
Then the client sends the second packet i.e. P1, waits for another acknowledgement, and so on.
In the Blast protocol the client will send all the packets as soon as possible.
The server acknowledges the entire message when all the packets have been received.

## Slide 11: Stop-and-Wait
Receiver: send an acknowledge (ACK) back to the sender upon receiving a packet (frame)
Sender: excepting first packet, send a packet only upon receiving the ACK for the previous packet
Time
Sender
Receiver
frame
frame
ACK
ACK

## Slide 12: What Can Go Wrong?
Sender
Receiver
frame
frame
ACK
Timeout
Frame lost  resent it
on Timeout
Sender
Receiver
frame
frame
ACK
ACK
Timeout
ACK lost  resent packet
Need a mechanisms to
detect duplicate packet
Sender
Receiver
frame
frame
ACK
ACK
Timeout
ACK delayed  resent packet
Need a mechanism to differentiate
between ACK for current
and previous packet

## Slide 13: Stop-and-Wait Disadvantage
May lead to inefficient link utilization
Example: assume
  One-way propagation = 15 ms
  Bandwidth = 100 Mbps
  Packet size = 1000 bytes  transmit = (8*1000)/108 = 0.08ms
  Neglect queue delay  Latency = approx. 15 ms; RTT = 30 ms
Propagation = 15 ms
Bandwidth = 100 Mbps

## Slide 14: Stop-and-Go Disadvantage cont.
Send a message every 30 ms  Throughput = (8*1000)/0.03 = 0.2666 Mbps
Thus, the protocol uses less than 0.3% of the link capacity!
Sender
Receiver
frame
frame
ACK
ACK
30 ms
30 ms

## Slide 15: How to Keep the Pipe Full?
Send multiple packets without waiting for first to be acked
  Number of pkts in flight = window
Reliable, unordered delivery
  Several parallel stop & waits
  Send new packet after each ack
  Sender keeps list of unack’ed packets; resends after timeout
  Receiver same as stop & wait
How large a window is needed?

## Slide 16: Cont..
With stop and wait protocol, if a packet is damaged or lost, the client fails to receive an acknowledgement on time, so it retransmits the one bed packet.
With the blast protocol, the server is faced with a decision when, say, Packet 1 is lost but Packet 2 subsequently arrives correctly.
It can abandon everything, waiting for the client to timeout out and retransmit the entire message.
Or alternatively, it can buffer Packet 2 (along with 0), hope that Packet 3 comes in correctly, and then specifically ask the client to send it Packet 1. This technique is called Selective repeat.
Along with error control, another major point of concern is flow control.
Many network interface chips are able to send consecutive packets with almost no gap between them, but they are not always able to receive an unlimited number of back to back packets due to finite buffer capacity on chip.

## Slide 17: Cont..
With some designs, a chip cannot even accept two back to back packets because after receiving the first one the chip is temporarily disabled during the packet-arrived interrupt, so it misses the start of the second one.
When a packet arrives and the receiver is unable to accept it, an overrun error occurs and the incoming packet is lost.
With stop-and-wait protocol, overrun errors are impossible.
With the blast protocol, receiver overrun is a posssibility. To deal with overrun error in blast protocol, the following mechanism can be used:
If, on the one hand, the problem is caused by the chip being disabled temporarily while it is processing an interrupt, a smart sender can insert a delay between packets to give the receiver just enough time to generate the packet-arrived interrupt and reset itself.
If the required delay is short, the sender can just loop (busy waiting); if it is long, it can set up a timer interrupt and do something else while waiting.
If it is in between, probably the best solution is busy waiting.
If, on the other hand, the overrun is caused by the finite buffer capacity of the network chip, say n packets, the sender can send n packets, followed by a substantial gap.

## Slide 18: Sliding Window Protocol: Sender
Each packet has a sequence number
  Assume infinite sequence numbers for simplicity
Sender maintains a window of sequence numbers
  SWS (sender window size) – maximum number of packets that can be sent without receiving an ACK
  LAR (last ACK received)
  LFS (last frame sent)
seq. numbers
LAR
LFS
Acknowledged packets
Packets not acknowledged yet

## Slide 19: Example
Assume SWS = 3
Sender
Receiver
frame 1
1
frame 2
frame 3
2
3
1
ACK 1
2
3
1
frame 4
2
3
4
1
ACK 2
frame 5
2
3
4
5
1
Note: usually ACK contains the sequence number of the first packet in
sequence expected by receiver

## Slide 20: Sliding Window Protocol: Receiver
Receiver maintains a window of sequence numbers
  RWS (receiver window size) – maximum number of out-of-sequence packets that can received
  LFR (last frame received) – last frame received in sequence
  LAF (last acceptable frame)
  LAF – LFR <= RWS

## Slide 21: Sliding Window Protocol: Receiver
Let seqNum be the sequence number of arriving packet
If (seqNum <= LFR) or (seqNum >= LAF)
  Discard packet
Else
  Accept packet
  ACK largest sequence number seqNumToAck, such that all packets with sequence numbers <= seqNumToAck were received
seq. numbers
LFR
LAF
Packets in sequence
Packets out-of-sequence

## Slide 22: Sender/Receiver State
Receiver
Sender
…
…
Sent & Acked
Sent Not Acked
OK to Send
Not Usable
…
…
Max acceptable
Receiver window
Max ACK received
Next seqnum
Received & Acked
Acceptable Packet
Not Usable
Sender window
Next expected

## Slide 23: Sequence Numbers
How large do sequence numbers need to be?
  Must be able to detect wrap-around
  Depends on sender/receiver window size
E.g.
  Max seq = 7, send win=recv win=7
  If pkts 0..6 are sent succesfully and all acks lost
    Receiver expects 7,0..5, sender retransmits old 0..6!!!
Max sequence must be  send window + recv window
Notes: Xxx picture

## Slide 24: Cumulative ACK + Go-Back-N
On reception of new ACK (i.e. ACK for something that was not acked earlier)
  Increase sequence of max ACK received
  Send next packet
On reception of new in-order data packet (next expected)
  Hand packet to application
  Send cumulative ACK – acknowledges reception of all packets up to sequence number
  Increase sequence of max acceptable packet

## Slide 25: Loss Recovery
On reception of out-of-order packet
  Send nothing (wait for source to timeout)
  Cumulative ACK (helps source identify loss)
Timeout (Go-Back-N recovery)
  Set timer upon transmission of packet
  Retransmit all unacknowledged packets
Performance during loss recovery
  No longer have an entire window in transit
  Can have much more clever loss recovery

## Slide 26: Go-Back-N in Action

## Slide 27: Selective Ack + Selective Repeat
Receiver individually acknowledges all correctly received pkts
  Buffers packets, as needed, for eventual in-order delivery to upper layer
Sender only resends packets for which ACK not received
  Sender timer for each unACKed packet
Sender window
  N consecutive seq #’s
  Again limits seq #s of sent, unACKed packets

## Slide 28: Selective Repeat: Sender, Receiver Windows

## Slide 29: Summary of ARQ Protocols
Mechanisms:
  Sequence number
  Timeout
  Acknowledgement
Sender window: fill the pipe
Receiver window: handle out-of-order delivery

## Slide 30: Many Nuances
What type of acknowledgements?
  Selective acknowledgement
  Cumulative acknowledgement
  Negative acknowledgement
How big should be the timeout value, Sliding Window Size (SWS), Receiving Window Size (RWS), sequence number field?
Reliability mechanism used to implement other functions: flow control, congestion control
  Function overloading introduces ambiguity and complexity

## Slide 31: #9.3: Critical Path
A critical path is defined as the sequence of instructions that is executed on every RPC (Eg. A client to a remote server)
There are 14 steps in the RPC from Client-to-Server
  Call stub 8. Move packet to controller over the QBus
  Get message buffer 9. Ethernet transmission time
  Marshal parameters 10. Get packet from controller
  Fill in headers 11. Interrupt service routine
  Compute UDP checksum 12. Compute UDP Checksum
  Trap to Kernel 13. Context switch to user space
  Queue packet for transmission 14. Server stub code

## Slide 32: #9.3: Critical Path : Schematic View
*
C
Call stub procedure
Perform service
Prepare message buffer
Marshal parameters into buffer
Fill in message header fields
Trap to kernel
Call server
Set up parameters on stack
Unmarshal parameters
Context switch to kernel
Copy message to kernel
Determine destination address
Put address in message header
Set up network interface
Start timer
Context switch to server stub
Copy message to server stub
See if stub is waiting
Decide which stub to give it to
Check packet for validity
Process interrupt
Client Machine
Server Machine
Server
Server
stub
Kernel
Client
Client
stub
Kernel

## Slide 33: #9.4: Copying
Copy is an issue in RPC [ it dominates execution time in RPC]
Q: Why does this issue occur in RPC? [ In most of the systems the kernel and the user address spaces are disjoint. A message must be copied 1-to-8 times depending on the h/w, s/w and type of call].
Analysis: In general a message is required to be copied many times during RPC communication. It hampers the performance of the execution time of the RPC.
The 8-different copies degrades the performance of RPC.

## Slide 34
The network chip can DMA the message directly out of the client stub’s address space onto the network, depositing it in the server’s kernel memory.
Then the server kernel inspects the packet and maps the page into the server’s address space. If kernel can’t map the page into the server’s address space, then kernel copies the packet to the server stub
The hardware is started, causing the packet to be moved over the network to the interface board on the destination machine
When the packet arrived, interrupt occurs, kernel copies it to its buffer (before knowing its exact loaction)
Finally, the message has to be copied to the server stub
If(the call has a large array passed as a value parameter) the array has to be copied onto the client’s stack for the call stub,
Copy from the stack to the message buffer during marshaling within the client stub
Copy from the incoming message in the server stub to the server’s stack preceding the call to the server.
Copy
1
Copy
2
Copy
3
Copy
4
Copy
5
Copy
6
Copy
7
Copy
8
8 copies
Performance degrades
MANDATORY
COPIES

## Slide 35: #9.4: Copying Cont.
How to eliminate unnecessary copying?
  Using the hardware scatter-gather.
  A N/W chip that can do scatter-gather can be set up to assemble a packet by concatenating two or more memory buffers.
  At the Sender’s side: The kernel can built the reusable packet header inside the kernel space, leaving the user data in client stub, with the hardware pulling them together as the packet goes out the door. Being able to gather up a packet from multiple sources eliminates copying.
  At the Receiver’s side: Similiarly, being able to scatter the header and body of an incoming packet into different buffers also helps on the receiving end.
  In Operating Systems: Using virtual memory
  Using mapping: If(memory map can be updated in less time)
    Then, mapping is faster than copying
    Else, Not
*****

## Slide 36: #9.5: Timer Management
Timer: It is an automatic mechanism for activating an entity at a preset time.
Setting a timer requires building a data structure specifying when the timer is to expire and what is to be done when that happens.
The list of messages are in sorted order
Timer starts just after message transmitted
If(ACK or Reply arrives before the timer expires)
  Then the timeout entry must be located and removed from the list
Timer value should be neither too high or too low
Most systems maintains a Process Table to implement Timer

## Slide 37: #9.5: Timer Management via Sorted List and Process Table
*
Current time
Current time
14200
14200
14205
14216
0
14212
14205
14212
14216
Process 3
Process 2
Process 0
0
1
2
3
(a) Timeouts in a sorted list
(b) Timeouts in a process table
0
Timer is off
Explanation: In process table instead of storing timeouts in a sorted linked list, each process table entry has a field for holding its timeouts.
Working Principle: The kernel scans the entire process table, checks each timer value against the current time. If (Tread<=Tcurrent) then it is processed and reset.
Note: Sweep Algorithms operates by periodically making a sequential pass through a process table.
Sorted List w.r.t.
time out

## Slide 38: Q&A

## Slide 39: Practice Questions
How an Operating System avoid copy of a message during RPC? (Pg-93)
Suppose that the time to do a null RPC (i.e., 0 data bytes) is 1.0 msec, with an additional 1.5 msec for every 1K of data. How long does it take to read 32K from the file server in a single 32K RPC? How about as 32 1K RPCs? (Pg. 117)

## Slide 40: Thank You!